## Slide 1
cv
CostVision
CAD-TO-COST INTELLIGENCE
The 3D Viewer — and the Data It Captures
How leading should-cost tools turn CAD into cost, what our viewer and geometry engine do today, and what is still to build.
Market study
Where we stand
Roadmap
What is built now
CostVision · Cost Engineering & Digital Innovation · Study July 2026, updated September 2026
Notes: This deck started in July as an answer to a fair challenge. Someone had seen a rival should-cost tool and liked its 3D viewer. It felt like real CAD software, and it seemed to pull data straight off the model. So I did two things. I read up on how the leading tools do this, and I went through our own viewer and geometry engine line by line. Since July we have built a good part of that plan. So I've updated the deck to say plainly what is in the tool today and what is still future. One thing to hold on to all the way through. At JLR the AI is switched off. The CAD path runs on measured geometry and plain rules. Where the geometry can't decide something, the tool asks the engineer. Nothing on these slides depends on AI.

## Slide 2
cv
CostVision
CAD-TO-COST INTELLIGENCE
EXECUTIVE SUMMARY
What we found
CostVision · CAD viewer study & roadmap · Updated September 2026 · Confidential
1
The pattern is the same everywhere
The leading tools find features on the CAD solid (the B-rep: its exact faces and edges), turn them into cost drivers, and let a person correct the result instead of retyping the part.
2
We already had the hard part
Our geometry engine measures volume, size, walls, holes, draft and setups. Rules turn that into cost inputs. Where the geometry cannot decide, the tool asks the engineer.
3
The "CAD feel" is analysis on the model
Wall thickness and draft coloured on the part, sections, a model tree and a big canvas. Since July most of this has been built into our viewer.
4
What is left is deeper capture
Tolerances read from the CAD file, more feature types and a better STL path are still roadmap. Browser-side B-rep and learned recognition are future research.
Notes: If you remember four things, make it these. One, the leading tools all work the same way. They find features on the solid model, the B-rep, which just means the exact faces and edges of the part. They turn those features into cost drivers, and a person corrects the result rather than retyping the part. Two, we already had the hard part. Our geometry engine measures the part, and rules turn those measurements into cost inputs. When the geometry can't settle something, like the process route or the material family, the tool asks you. Three, the thing that makes a viewer feel like CAD software is analysis drawn on the model. Most of that is now built. Four, what is left is deeper capture: tolerances from the file, more feature types, and a better answer for STL files. Those are still roadmap, and I'll be clear about that on each slide.

## Slide 3
cv
CostVision
CAD-TO-COST INTELLIGENCE
THE PATTERN · FROM PUBLIC MATERIAL
How the leading tools turn CAD into cost
CostVision · CAD viewer study & roadmap · Updated September 2026 · Confidential
3D model
STEP, native CAD or Parasolid file
→
Feature finding
find holes, pockets, bends, ribs, undercuts (AFR: automatic feature recognition)
→
Cost drivers
each feature maps to a route, operations and tooling
→
Person corrects
fix a feature that was read wrong; no retyping the part
→
Should-cost
built up from the drivers, so it can be explained
aPriori — geometric cost drivers
As aPriori describes it, the tool reads the 3D model, breaks it into individual geometric cost drivers, and builds the cost from the bottom up.
It can cost from STEP and Parasolid files, which carry no feature history. That suggests it reads the shape itself rather than replaying how the designer built it. Tolerances can be added to drivers to steer the process route.
Siemens NX Feature2Cost
As Siemens describes it, commodity modules (moulding, stamping) analyse the geometry and pick out part dimensions, ribs, undercuts, bends and progressive-die features.
Those become cost drivers. The user can correct them, and they pass into Siemens' own product-costing software.
Source: each vendor's public product material and blogs, read July 2026. Not tested hands-on by us.
Notes: This is the mental model for the rest of the deck. Read it left to right. A 3D model comes in. Software finds the features, the holes, pockets, bends, ribs and undercuts. People call this AFR, automatic feature recognition. Each feature maps to a cost driver, like an operation or a tool. A person steps in only to fix a feature that was read wrong. Out comes a cost you can explain line by line. The two cards are how aPriori and Siemens describe their own tools in public. I haven't tested either of them hands-on, so treat this as their account, not mine. The part I find useful is that both keep a person in the loop to correct the recognition. Nobody claims to be fully hands-off. That matches how we work: the tool measures, and when it isn't sure, it asks.

## Slide 4
cv
CostVision
CAD-TO-COST INTELLIGENCE
THE LANDSCAPE
Capability comparison
CostVision · CAD viewer study & roadmap · Updated September 2026 · Confidential
B-rep feature
recognition
On-model DFM
overlays
Tolerances from
CAD → cost
CAD-software
viewer feel
CAD → cost with
no retyping
Web /
instant
Tool
aPriori
Siemens NX F2C
3D-Tool (viewer)
Werk24 (drawings)
MTI Costimator 3DFX
CostVision — today
CostVision — if roadmap lands
Full
Partial
Limited / none
Other tools: our own read of public material (July 2026), not a hands-on test. CostVision rows: checked against the code, September 2026.
Notes: This is the map. Each column is a capability that matters, each row is a tool. A full cyan dot means strong, amber means partial, and hollow means limited or missing. Please take the other rows as my reading of their public material, not a test. The costing leaders are strong on feature recognition and on going from CAD to cost without retyping. The best pure viewer experience comes from 3D-Tool. Werk24 reads tolerances, but from 2D drawings. Now our row. Since July we've filled in on-model analysis and the CAD feel, so those are full now. Feature recognition is only partial. We find holes, bosses, fillets and some pockets, but not chamfers, slots or thread specs. Tolerances from the CAD file is still empty. The bottom row is what we'd have if the roadmap lands. It is a plan, not a promise.

## Slide 5
cv
CostVision
CAD-TO-COST INTELLIGENCE
THE EXPERIENCE
What makes a viewer "feel like CAD software"
CostVision · CAD viewer study & roadmap · Updated September 2026 · Confidential
It is not prettier rendering. It is analysis drawn on the model, and room to work. 3D-Tool, a dedicated viewer, is a good example of the idea.
Wall-thickness heatmap
Thin and thick areas coloured on the part. It shows moulding and casting risk at a glance. We have this today for STEP and IGES.
Draft & undercut view
Each face shaded by its draft angle to the tool pull direction. Undercuts need slides, and slides cost money. We have this today.
Section & measure
Cut planes and true measurements: the everyday CAD actions people expect. We have cut planes on X, Y and Z and six measure tools.
Feature / model tree
A list of bodies and features. Click a row and the faces light up. We have this today for STEP and IGES.
Tolerances on the model
Tolerances and notes shown in 3D (PMI: product manufacturing information), tied to the faces they apply to. We do not have this yet.
A big, easy canvas
A large view, an orientation cube and smooth orbit. We have an Expand button, the cube and standard views today.
Notes: When people say a viewer feels like CAD software, this is usually what they mean. It isn't about nicer graphics. It's analysis painted on the model. The biggest one is a wall-thickness heatmap. Thin and thick areas show up in colour, and you can see moulding or casting risk straight away. Then draft and undercut. You shade each face by how well it releases from the tool, and undercuts show up in red, because they need slides and slides cost money. Then the everyday actions: cut planes, measuring, and a model tree where clicking a row lights up the faces. Most of these are now in our viewer, and each card says so. The one we don't have is tolerances shown on the model. PMI just means product manufacturing information, the tolerances and notes stored in the CAD file. We can't read those yet.

## Slide 6
cv
CostVision
CAD-TO-COST INTELLIGENCE
OUR BASELINE · CHECKED AGAINST THE CODE, SEPTEMBER 2026
Where CostVision stands today — honestly
CostVision · CAD viewer study & roadmap · Updated September 2026 · Confidential
In the tool today
STEP/IGES measured by OpenCASCADE; STL by a fast mesh path: volume, weight, size, area
Feature table (STEP/IGES): holes and bosses with diameter and depth; fillets; cautious pockets
Wall thickness by ray-casting, draft and undercut counts, setup count, sheet-metal bends
CNC cycle-time estimate for STEP/IGES, built up from the measured features
Viewer: orientation cube, model tree, X/Y/Z section planes, exploded view, Expand
On-model colour: wall thickness, draft and undercut, and £ per face after a costing
Measure: distance, radius, angle, point, face-to-face; export to CSV
Click a face for its exact type, radius and area; the matching result rows are outlined
Still open
No tolerances read from the CAD file (STEP AP242 PMI); the engineer types the tightest tolerance
STL has no feature table: no cycle time, tree or thickness map; the engineer types the cycle time
No chamfer, slot or thread-spec recognition yet
The browser shows a mesh; the server turns STEP into triangles (no live B-rep in the browser)
Section planes have no solid caps on the cut
Extrusion has no CAD rules yet (its form still costs it)
Route or material is asked, not guessed, when geometry cannot decide: by design, but it is typing
No estimate has yet been compared with a price JLR actually paid
Notes: I want to be straight about where we are, because the rest of the deck depends on it. On the left is what's in the tool today, and I checked each line against the code. The geometry engine is OpenCASCADE, an open-source CAD kernel. It measures the part, finds holes, bosses and fillets, and for STEP files it builds up a machining cycle time. The viewer now has the cube, the model tree, sections, exploded view, and colours for thickness, draft and cost per face. On the right is what's still open. The big ones are capture. We don't read tolerances from the CAD file. STL files have no feature table, so the tool stops and asks you for a cycle time rather than invent one. And there's one gap that matters more than any feature. We have not yet compared an estimate with a price JLR actually paid.

## Slide 7
cv
CostVision
CAD-TO-COST INTELLIGENCE
WHERE THE LEVERAGE IS
The two ideas behind the plan
CostVision · CAD viewer study & roadmap · Updated September 2026 · Confidential
“We measured it —
now we show it.”
In July the engine already worked out wall thickness, draft and undercuts, but the viewer never drew them. Now thickness, draft and £ per face are coloured on the model. The data was there; the viewer just uses it.
“Capture more —
so people type less.”
Every feature read from the CAD is one less field someone fills in, and one less place for a typing slip. Tolerances, chamfers, slots and threads are next. Until then, the tool asks the engineer.
The rule we keep: the viewer is a place to capture and check cost inputs, not decoration. The tool measures and calculates; every £ traces to a rate. AI never sets a price, and at JLR it is switched off.
Notes: The whole plan comes down to two ideas. The first one is mostly done. In July the engine was already working out wall thickness, draft and undercuts, and then throwing them away as far as the viewer was concerned. Now they're coloured on the model, along with the cost per face after you run a costing. That was cheap to build because the numbers already existed. The second idea is still ahead of us. Every feature we can read from the CAD file is a field nobody has to type. Tolerances, chamfers, slots and threads are next. Until we can read them, the tool asks the engineer, and I think that's the right default. And the rule at the bottom doesn't change. The viewer is there to capture and check inputs. The tool measures and calculates. AI never sets a price, and at JLR it's switched off anyway.

## Slide 8
cv
CostVision
CAD-TO-COST INTELLIGENCE
FUTURE OPTIONS · PUBLISHED AND OPEN SOURCE
The technology we could build on
CostVision · CAD viewer study & roadmap · Updated September 2026 · Confidential
occt-import-js (OpenCASCADE in the browser)
An open-source build of our CAD kernel that runs in a web page (WebAssembly). It opens STEP and IGES directly and links each triangle back to its original face, so a click could select an exact face with no server call.
OpenCASCADE XDE — STEP AP242 PMI
The same kernel has a module that reads tolerances, dimensions and datums stored in STEP AP242 files. That is the route to reading tolerances from the 3D file, not a separate drawing.
Learned feature recognition (research)
Published research models (UV-Net, BRepGAT, BrepMFR, AAGNet) treat the B-rep as a graph of faces and label machining features face by face. Papers report 98–99% on public benchmarks.
Heatmap methods (textbook)
Wall thickness: cast a ray inward from each face. Draft: angle between the face normal and the pull direction. We already use both, in the engine and on the model.
Honest caveat: the 98–99% figures are research results on clean, synthetic datasets, not our results. Real STEP files are messier, so a person would always check what the model finds.
Notes: None of the future work needs inventing. It's all published, and most of it is open source. First, occt-import-js. It's the same CAD kernel we run on the server, compiled to run inside a web page. It could open a STEP file in the browser and tie every triangle back to its original face. Second, the kernel has a module that reads tolerances from STEP AP242 files. AP242 is the newer STEP standard that can carry tolerances inside the 3D file. Third, there's academic work on learned feature recognition. Those papers report 98 to 99 percent on public benchmarks. Please don't read that as a number for us. It's research on clean, synthetic parts, and real CAD is messier. So a person would still check the result. Fourth, the heatmap methods are textbook, and we already use them. So this slide is options, not commitments.

## Slide 9
cv
CostVision
CAD-TO-COST INTELLIGENCE
ROADMAP · STATUS SEPTEMBER 2026
The build plan — four phases, and where each stands
CostVision · CAD viewer study & roadmap · Updated September 2026 · Confidential
Phase 0
Quick wins
Bigger viewer, and draw the data we already measured: thickness, draft, model tree, result-to-model links.
Built
→
Phase 1
CAD-software feel
Orientation cube, exploded view, X/Y/Z sections, richer measuring, £ per face. Solid section caps still to do.
Mostly built
→
Phase 2
Deeper capture
Fillets and cautious pockets found today. Chamfers, slots, threads, STL features and tolerances from STEP AP242 still to do.
Partly started
→
Phase 3
Research track
Browser-side B-rep kernel and learned feature recognition. Not started and not committed.
Future
Each phase ships on its own. The two things you asked for — a bigger viewer and a CAD-software feel — were Phases 0 and 1, and both are now in the tool.
Notes: Here's the plan from July, with where each phase stands today. Phase zero was the quick wins. Make the viewer bigger, and draw the data the engine already measured. That's built. Phase one was the CAD-software feel. The cube, exploded view, sections, better measuring, and colouring the model by cost. That's mostly built. The one piece left is solid caps on a section cut, so a sliced part looks solid rather than hollow. Phase two is deeper capture, and it has only just started. We find fillets, and pockets in a cautious way. Chamfers, slots, thread specs, anything on STL, and tolerances from the file are all still to do. Phase three is research. A CAD kernel in the browser and learned recognition. It's not started and I'm not committing to it. The good news is that both of the things you asked for are now in the tool.

## Slide 10
cv
CostVision
CAD-TO-COST INTELLIGENCE
ROADMAP · BUILT
Phase 0 — Quick wins
CostVision · CAD viewer study & roadmap · Updated September 2026 · Confidential
All five quick wins from the July plan are now in the tool. Three of them only needed us to draw data the engine already measured.
Bigger viewer
An Expand button fills the window with the model. Esc takes you back to the costing layout.
Built. It fills the browser window; it does not use the operating system's full-screen mode.
Wall-thickness heatmap
Per-face thickness from the geometry engine, coloured from thin (red) to thick (blue).
Built. STEP and IGES only; an STL has no per-face data.
Draft / undercut view
Faces shaded by draft against a chosen pull direction (X, Y or Z). Undercuts show in red.
Built. Works on any file, as it uses the mesh.
Model tree
Bodies, features and face types. Click a row and its faces light up; show or hide each body.
Built. STEP and IGES only.
Result ↔ model link
Click a face and the matching feature rows in the result are outlined. A warning's "show me" button lights up its faces.
Built. Works where the feature has face data (STEP/IGES).
Notes: Phase zero is done, so this slide is really a checklist. The first ask was a bigger viewer. There's now an Expand button that fills the window, and Esc brings you back. To be precise, it fills the browser window rather than switching the whole screen into full-screen mode. Then the three overlays. Wall thickness coloured red for thin and blue for thick. Draft and undercut against a pull direction you choose. And a model tree where clicking a row lights up the faces. Thickness and the tree need a STEP or IGES file, because an STL is just triangles with no face data. Last, the link between the result and the model. Click a face and the matching rows in the result get outlined. If a warning is about specific faces, its show-me button highlights them. It means you can see where a number came from.

## Slide 11
cv
CostVision
CAD-TO-COST INTELLIGENCE
ROADMAP · MOSTLY BUILT
Phase 1 — The CAD-software feel
CostVision · CAD viewer study & roadmap · Updated September 2026 · Confidential
Orientation cube + views
Built. A cube in the corner: click a face or axis to snap to that view. Home, front, top, right and fit buttons.
Model tree
Built. Bodies, found features and face types, with show and hide for each body.
Exploded view
Built. Pull a multi-body file apart radially or along X, Y or Z. Each component can also be moved or rotated.
Section planes
Partly built. Independent cut planes on X, Y and Z. Solid caps on the cut face are still to do.
Richer measuring
Built. Distance (snaps to corners and edges), 3-point radius, angle, X/Y/Z point, face-to-face. Saved per file; export to CSV.
Cost on the model
Built. After a CAD costing, faces are coloured by the £ of the machining lines they carry.
Where this leaves us: the viewer is now a place to check the cost, not just a preview. The limits: it shows a mesh, sections have no caps, and tolerances are not read from the file.
Notes: Phase one was about making it feel like CAD software, and most of it is in. The orientation cube is in the corner. Click a face of it and the view snaps round. The model tree lists bodies, features and face types, and you can hide bodies. Exploded view pulls a multi-body file apart, and you can move or rotate each component. Section planes work on all three axes at once. What's missing is a solid cap on the cut, so today a sectioned part looks hollow. Measuring is much richer than in July. Distance that snaps to corners and edges, radius from three points, angle, a coordinate read-out, and face-to-face distance. And after a CAD costing, the model is coloured by how much money sits on each face. So the viewer is now somewhere you check the cost. It's still a mesh, though, and it still can't read tolerances.

## Slide 12
cv
CostVision
CAD-TO-COST INTELLIGENCE
ROADMAP · PARTLY STARTED
Phase 2 — Deeper automatic capture
CostVision · CAD viewer study & roadmap · Updated September 2026 · Confidential
More features found → cost
Fillets: found today. Turning them into finishing operations is still to do
Pockets and machined flat faces: found cautiously, and off in the cost until the engineer confirms
Chamfers, slots and thread specs (pitch and class): still to do
Rib count on mouldings to drive tool complexity: still to do
Machined vs as-cast faces: still to do. Today a guard caps machining time on near-net parts
STL features: still to do. Today the tool stops and asks for a cycle time
Tolerance-driven costing (future)
Not built. The idea: read tolerances (GD&T: geometric dimensioning and tolerancing) from STEP AP242 files, and map them to process and inspection. Today the engineer types the tightest tolerance, and it scales the machining time.
Tight bore tolerance
→ ream / hone / grind added
Fine surface finish (Ra)
→ extra finishing operation
Flatness / position GD&T
→ inspection + fixturing cost
Loose general tolerance
→ cheaper route, faster cycle
Notes: Phase two is about capturing more so people type less, and it has only just started. On the left, the engine now finds fillets. It also finds pockets and machined flat faces, but cautiously. They're switched off in the cost until the engineer confirms them, because a wrong pocket adds cost that isn't real. Chamfers, slots, thread specs and rib counts are still to do. So is the STL path. Today, if you upload an STL for a machined part, the tool stops and asks you for a cycle time rather than making one up. On the right is tolerance-driven costing, and this is future work. GD&T means geometric dimensioning and tolerancing. The idea is to read it from the STEP file and let a tight bore add a reaming or grinding step. Today the engineer types the tightest tolerance on the form, and that scales the machining time.

## Slide 13
cv
CostVision
CAD-TO-COST INTELLIGENCE
ROADMAP · FUTURE, NOT STARTED
Phase 3 — Research track
CostVision · CAD viewer study & roadmap · Updated September 2026 · Confidential
CAD kernel in the browser (occt-import-js)
Open STEP and IGES directly in the browser and keep the real B-rep, not a mesh made on the server. That would allow exact face measurement, faster loading, and face picking with no server call.
What it would change: every face becomes an exact object you can click and cost, even before the server replies.
Learned feature recognition
Add a research-style model (the UV-Net / BRepGAT family) that labels machining features face by face. It could pick up compound features our current rules miss.
What it would change: better recall on complex parts, and every label is still a face a person can check. Only worth it if it holds up on real JLR parts.
Why this comes last
It is the most effort, and the published accuracy comes from synthetic test data. It only makes sense once Phase 2 is done and we have real JLR parts to test it on. A learned model would only label features. The cost would still be plain arithmetic, and at JLR any AI would need approval first.
Notes: Phase three is research, and I've put it last on purpose. None of it is started. The first idea is to run the CAD kernel inside the browser, so the viewer holds the real faces rather than a mesh the server made. That would make measuring exact and picking a face instant. The second is a learned model that labels machining features face by face. It might catch compound features our rules miss. But I want to be careful here. The accuracy figures in the papers come from clean, synthetic parts. We'd only know whether it helps by testing it on real JLR parts. And it would only ever label features. The money would still be plain arithmetic on rates. At JLR, anything like this would also need AI approval, which we don't have. So this stays a research track until Phase two is done.

## Slide 14
cv
CostVision
CAD-TO-COST INTELLIGENCE
WHAT YOU ASKED FOR, CHECKED AGAINST THE TOOL
Your two asks — where they stand
CostVision · CAD viewer study & roadmap · Updated September 2026 · Confidential
1 · Make the 3D viewer bigger
Built: Expand button fills the window with the viewer
Built: Esc returns to the costing layout
Built: the tools bar can be hidden to give the model room
Built: toolbar groups can be dragged into your own order
Built: the model-tree panel can be resized
Not yet: true operating-system full-screen mode
2 · A CAD-software feel
Built: orientation cube and standard views
Built: model tree; click a row and its faces light up
Built: thickness, draft and undercut colours on the model
Built: X/Y/Z sections and exploded view (no solid caps yet)
Built: radius, angle, point and face-to-face measuring
Built: £ per face after a CAD costing
Notes: This slide takes the two things you asked for and checks them against the tool as it is today. On the left, the bigger viewer. There's an Expand button, Esc brings you back, you can hide the tools bar, drag the toolbar groups into your own order, and resize the model tree. The one thing I'd call not done is true full-screen mode. Today it fills the browser window, which in practice is most of the screen. On the right, the CAD feel. The cube, the model tree, the colour overlays, sections and exploded view, the measuring tools, and cost per face are all in. The honest footnote is the section caps, and that most of the richer features need a STEP or IGES file rather than an STL. So both asks are met. The remaining work is about capture, not the viewer.

## Slide 15
cv
CostVision
CAD-TO-COST INTELLIGENCE
BENEFITS AND NEXT STEPS
Why it matters, and what I recommend next
CostVision · CAD viewer study & roadmap · Updated September 2026 · Confidential
Less typing
Each feature read from the CAD is a field nobody types. Where geometry cannot decide, the tool asks.
Fewer slips
A measured value cannot be mistyped. Every input traces back to the geometry or a rate.
Design issues seen early
Thin walls, zero draft and undercuts show on the model while a change is still cheap.
Easier to explain
Click a face to see what was measured, and where the money sits. The model backs up the number.
Tolerance-aware cost (future)
Reading GD&T from the file would price precision parts from the model itself. Not built yet.
Still traceable
The tool measures and calculates. AI never sets a price, and at JLR it is switched off.
Recommendation
Use what is built on real JLR parts, and log actual prices so we learn how close the estimates are. Next build: solid section caps, then chamfer, slot and thread recognition, and a better STL path. Tolerances from STEP AP242 after that. Phase 3 stays a research track.
Notes: Let me finish on why this matters and what I'd do next. The benefits are simple. Every feature we read from the model is a field nobody types, and a measured value can't be mistyped. Thin walls and undercuts show up while a design change is still cheap. And when someone asks where a number came from, you can click the face and show them. I haven't put a time saving or an accuracy figure on any of this, because we haven't measured one. That's the first part of my recommendation. Use what's built on real JLR parts, and log the actual prices you pay, so we find out how close the estimates really are. Then the next build: section caps, chamfers, slots and threads, and a better answer for STL files. Tolerances from the STEP file after that. Phase three stays research until we have a reason to start it.

## Slide 16
cv
CostVision
CAD-TO-COST INTELLIGENCE
CAD-TO-COST · MEASURED, THEN RULES · STEP, IGES OR STL
What the Tool Measures — and Where It Goes
CostVision · CAD viewer study & roadmap · Updated September 2026 · Confidential
Measured from the geometry
→ Feeds this cost input
Volume (exact, from the solid)
Material mass · stock size
Weight = volume × density
Material cost
Bounding box / envelope
Machine size · stock · setups
Body count
Flags an assembly, not one part
Hole & boss table (Ø, depth)
Drill, bore and tap operations
Wall thickness
Route choice · mould & cast checks
Draft & undercuts
Tooling complexity (side actions)
Surface area
Area-driven operations
CNC cycle & setups (STEP/IGES)
Machining time baseline
When the geometry cannot decide
The rules ask the engineer instead of guessing: the process route, the material family, a hole count on an STL.
Thick-walled parts (walls over about 6 mm) are offered casting, forging, cast + machine or machining.
An STL has no feature table, so a machined STL waits until the engineer types a cycle time.
Sheet metal: upload a DXF flat pattern with the STEP, and the measured blank replaces the bounding box.
The golden rule
AI never sets a price. At JLR it is switched off. The CAD path runs on measured geometry and rules, for 13 commodities. Every £ is plain arithmetic, traceable to a rate.
Notes: This slide answers the practical question. What does the tool measure on its own, and where does each number go? You can upload STEP, IGES or STL. On the left is what the geometry engine measures, with nothing typed. On the right is the cost input it feeds. Volume and weight give material cost. The bounding box sizes the machine and the stock. The hole table becomes drilling and tapping. Wall thickness helps pick the route, and draft and undercuts drive tooling. For STEP and IGES there's also a machining cycle estimate. The box on the right is the part I like most. When the geometry can't decide, the tool asks you. An STL has no feature table, so it waits for you to type a cycle time. For sheet metal you can add a DXF flat pattern, and the measured blank is used. Thirteen commodities work this way, with no AI.