## Slide 1
cv
CostVision
SHOULD-COST ENGINEERING
CostVision and CAPEE
The case for automating cost input, and then costing in bulk
1
Feed CAPEE automatically, and prove it
CAPEE keeps doing the costing. CostVision measures the 3D model and fills in the numbers. We prove it on real JLR parts first.
2
Cost in bulk, unattended
A whole basket of parts costed in one run, with no AI. A person is asked only where the geometry cannot decide.
JLR Cost Engineering · September 2026
Notes: Thank you for the time. I want to walk you through two ways a tool we have built, CostVision, could work with CAPEE, and ask for a decision on the first one. The first option is simple. CAPEE keeps doing the costing. CostVision measures the 3D model and fills in the numbers CAPEE needs, and we prove that on our own parts. The second option comes later. It is costing a whole basket of parts in one run, unattended. Neither option needs AI. In the build we have given JLR, there is no API key yet. I will be straight about what the tool does today and what it does not. The biggest gap is that it has never been checked against a price JLR actually paid. There are also no dates in this pack. Nobody has sized this work yet, so any timeline I showed you would be made up. What I can show is the order the work has to happen in.

## Slide 2
cv
CostVision
SHOULD-COST ENGINEERING
THE DECISION
What we are asking for
Approve a proof of concept: Option 1, inside CAPEE, on our own parts
Let CostVision fill CAPEE's cost input for one part type, on 30 to 50 parts we have already bought. At the end we will know how close it gets, how often an engineer has to correct it, and how much time it saves. Option 2 follows once that is known.
Detail
What we want to do
Fill CAPEE's cost input from the 3D model, for one part type
What we need from JLR
30 to 50 parts with the price we paid, our own rate data, three answers from IT, and a team for the trial
What it costs to try
Our own engineering time. No licence and no new tool to learn. CAPEE still does the costing, but it has to be changed to take the numbers
What we will know at the end
A measured accuracy figure against real JLR prices, and a measured time per part
What we are NOT asking for
A decision on Option 2 today. It needs the accuracy answer first
The one thing to know before you decide
CostVision has never been checked against a price JLR has actually paid. Its arithmetic matches a hand calculation, but that is not the same thing. The proof of concept is what tells us how close it gets.
Notes: This is the ask, so I will put it first. I would like approval to run a proof of concept inside CAPEE, on one part type, using parts we have already bought. The table says what that involves. What we need from JLR is on the second row, and I will come back to it at the end. What it costs is our own time. There is no licence, and nobody has to learn a new tool, because CAPEE still does the costing on the same screens. CAPEE does have to be changed to accept the numbers, and that is JLR's side of the work. The amber box is the honest bit, and I would rather say it now than have it come out in questions. We have never compared this tool with a price we actually paid. We know the arithmetic is right, because it matches a hand calculation to under 0.01 percent. But right arithmetic on the wrong inputs is still wrong. That is what the trial finds out.

## Slide 3
cv
CostVision
SHOULD-COST ENGINEERING
THE PROBLEM
What costing a part looks like today
TODAY, BY HAND
The engineer opens the part in CAD, reads the drawing,
and types the numbers into CAPEE.
Boxes to fill, depending on the part type:
about 12 to about 70 on CostVision's own forms
Part weight, starting material weight, wall thickness,
hole and pocket counts, machine times, surface area,
tolerances, finish, heat treatment.
Two engineers costing the same part will not type the
same numbers. So one part gets two answers.
WITH COSTVISION
The engineer hands over the 3D model: STEP, IGES or STL.
Measured off the model:
volume, weight, size, surface area, walls, holes,
pockets, bosses, gear teeth, bends.
Asked of the engineer:
material family, tolerances, finish, heat treatment,
and anything else the shape cannot decide.
Fixed rules fill the form. Same part, same numbers,
every time.
Measuring is not AI
The 3D model is measured by software, the way a CMM measures a part. Fixed rules turn the measurements into cost inputs. The JLR build has no API key yet. There is an optional AI mode that can read drawings, but it needs a key, and even when it is on it never sets a price.
Notes: This is the problem we are trying to fix. Today an engineer opens the model, reads the drawing and types the numbers in. How many depends on the part. On CostVision's own forms it runs from about twelve values to about seventy. I have not counted CAPEE's screens, so take that as a guide. The time matters, but the second point matters more. Two engineers costing the same part will not type the same numbers. So we get two answers for one part and no way to say which is right. On the right is what the tool does. It measures the model. Fixed rules turn the measurements into the values the form needs. Where the shape cannot decide something, such as the material, it asks the engineer rather than guessing. The blue box is the point I would like people to hold on to. Measuring is ordinary geometry software, not AI. The JLR build has no API key yet. Everything on this slide works without it.

## Slide 4
cv
CostVision
SHOULD-COST ENGINEERING
CURRENT STATUS
Where CostVision is today
Checked against the software on 28 September 2026.
WORKING NOW
19 manufacturing processes, an assembly roll-up and a
49-module software cost model
13 of those costed straight from a CAD file
Same inputs, same answer, every time
Measures STEP, IGES and STL with no internet
Asks the engineer where the geometry cannot decide
Blocks the costing when the checks find a contradiction
Bulk run from a parts list, with no AI
Keeps every rate book, so a costing can be redone
Rate library of 16 June 2026: 328 materials, 178
machines, 42 labour grades, 20 regions
Windows package: no installer, admin rights or internet
2,438 automated tests; 6 real parts pinned
NOT THERE YET
Never compared against a price JLR has paid
No link into CAPEE yet
No JLR single sign-on; it has its own sign-in
The bulk run is a command-line tool, not a screen
A costing done on screen is kept only if it is saved
Extrusion has no CAD rules yet (its form still costs it)
An STL has no feature table, so a machined STL needs
its cycle time typed in
The built-in rates are not JLR rates until we load ours
AI features need an API key; none added yet
Still under active development
What changed since the last time I showed you this
The bulk run now exists, with no AI. Every rate book is kept, so a past costing can be redone. The bulk run uses the same geometry checks as a single part, takes a region and a volume, and covers gear. And a Windows package now runs on a locked-down laptop.
Notes: Before the options, this is honestly where the tool is. I checked every line on this slide against the software this week. On the left is what works today. It covers nineteen manufacturing processes, and thirteen of them can be costed straight from a CAD file. Same inputs always give the same answer. It measures models with no internet, which is the first thing IT security will ask about. It has a proper test net: 2,438 automated tests, and six real production parts pinned so that a change which moves any of them fails the build. On the right is what is not done. The top line is the important one and I will keep coming back to it. There is no link into CAPEE yet, and no JLR single sign-on. The bulk run works, but only from the command line. The blue box is what has changed since I last showed you this. Most of the gaps I listed for Option two then are now closed. I will show you which on slide fifteen.

## Slide 5
cv
CostVision
SHOULD-COST ENGINEERING
SEQUENCE
The plan: prove it small, then scale it
Option 1
Fill CAPEE automatically
Prove it
On 30 to 50 real JLR parts
Decide
With an accuracy figure in hand
Option 2
Cost the whole basket in bulk
OPTION 1 · feed CAPEE automatically
CAPEE stays as it is and still does the costing.
Instead of typing a dozen to seventy boxes, the
engineer hands over the 3D model and checks what
fills in.
We hand over the measuring engine, the rules and
the checks. Slide 7 lists them.
OPTION 2 · cost in bulk, unattended
A list of parts goes in. Every one is measured, costed
and reported without anyone sitting there.
An engineer is asked only where the geometry
cannot decide.
The run is built. What is left is our rates, a trial,
and a screen for it if we want one.
Why this order
Option 1 is cheaper to try and gives the accuracy figure Option 2 needs. No sense costing 500 parts until one part is right.
Notes: This is the shape of the whole thing. We do Option one first, prove it on our own parts, look at the number, and then decide about Option two. Option one is the smaller change. CAPEE does not move. The engineer stops typing and starts checking. What we hand over is the measuring engine, the rules that fill the form, and the checks, and slide seven lists them. Option two is a different capability. Instead of costing the parts we have time for, we cost the whole basket. The run for that is already built, and it uses no AI. What is left is loading our own rates, trying it on a real basket, and maybe a screen for it. The reason for this order is on the green strip. Option one is cheap to try and it gives us the accuracy figure. There is no sense costing five hundred parts until we know the tool gets one part right.

## Slide 6
cv
CostVision
SHOULD-COST ENGINEERING
OPTION 1
Option 1: what happens to one part
What an engineer does each time they cost a part
Hands over the model
STEP, IGES or STL, from the CAPEE screen
Software measures
Size, weight, surface area, holes, pockets
Rules fill the form
Fixed rules turn measurements into values
Checks run
Contradictions are flagged or stop the cost
Engineer confirms
Material, tolerance, finish, heat treatment
CAPEE costs the part
CAPEE gets the numbers and calculates
What order the build has to happen in
Agree the connection
Stand up measuring
Hand over settings
Add safety checks
Connect into CAPEE
Trial on one part type
WE DO
Package the measuring software
Write out every setting
Move the safety checks across
Help with the CAPEE connection
JLR DOES
Tell us how CAPEE is built
Provide a server or laptop
Change CAPEE to take the numbers
Free up a team for the trial
One step we cannot size yet
Connecting into CAPEE depends on how CAPEE is built, and we do not know that yet. Slide 10 sets out the three ways of doing it.
Notes: This is Option one on a single slide. The top row is what happens each time somebody costs a part. The engineer hands over the 3D model from inside CAPEE. The software measures it. Fixed rules turn the measurements into the values CAPEE needs. The checks look for contradictions, and a serious one stops the costing until someone accepts it. The engineer confirms what a model cannot show, like material and heat treatment. Then CAPEE costs the part exactly as it does now. There is no AI anywhere in that row. Underneath is the build order and who does what. We package the software, write out the settings and bring the checks across. JLR tells us how CAPEE is built, provides a server or a laptop, and changes CAPEE to take the numbers. I have deliberately not put weeks against any of this. Nobody has sized it, and the connection step waits on an answer we do not have yet.

## Slide 7
cv
CostVision
SHOULD-COST ENGINEERING
OPTION 1 · HANDOVER
Option 1: what we hand over
Sizes counted in the source files on 28 September 2026, rounded. Both languages are in common use and JLR IT will have people who know them.
Part
Language
Size
What it does
Measuring engine
Python
about 2,500 lines
Opens the 3D model and measures it. Makes no internet connection.
Rules that fill the form
TypeScript
about 8,900 lines
Turn measurements into cost inputs and decide what the engineer is asked.
Geometry checks
TypeScript
about 400 lines
The checks on the next slide.
Bulk run
TypeScript
about 850 lines
A parts list in; results, open questions and a run record out. Option 2.
Settings list
Plain list
to be written
Every fixed number pulled together in one place. Slide 9.
JLR Rate Converter
Excel
no macros
Turns JLR's own rate card into the tool's format.
About the two languages
Python is the normal choice for engineering and measurement work. TypeScript is widely used for business software. Neither is unusual and neither ties JLR to one supplier.
One thing for IT to confirm
The measuring engine runs on a standard Linux server or from our Windows package. The cut-down Linux kind used for small services cannot run it.
Notes: You asked last time what would actually be handed over. Here it is, and the sizes come from counting the source files this week, rounded. The measuring engine is Python, the normal choice for measurement work. The rules and checks are TypeScript, which is common in business software. Neither is unusual, and neither ties JLR to us. The rules are the biggest piece. They turn the measurements into cost inputs and decide what to ask the engineer. The bulk run is there for Option two. The settings list does not exist yet as a separate file, and writing it is a step in the plan. The Rate Converter is an Excel workbook with no macros, which turns JLR's own rate card into the tool's format. The amber box is the practical point for IT. The measuring engine needs a standard Linux server or our Windows package. The cut-down Linux image cannot run it. That decides where this can live, so it is worth settling early.

## Slide 8
cv
CostVision
SHOULD-COST ENGINEERING
OPTION 1 · REQUIRED
Option 1: the checks that have to come with it
The price is always plain arithmetic. But a wrong input still gives a wrong cost. These four checks stop that, and they have to come across with everything else.
The measured model is the ground truth
Weight and size come from the model. Any figure fed to the cost that contradicts them is flagged. A weight gap of more than half stops the costing until an engineer accepts it.
The route has to fit the shape
A thick-walled part, walls over about 6 mm, is offered casting, forging, cast and machine, or machining. Never sheet metal or moulding.
Machining time has a ceiling
On a casting or forging, machining is capped at what finishing that part could realistically take, so a bad estimate cannot run the cost up.
Unknowns get asked, not guessed
Material family, heat treatment and tolerance class cannot be read off a solid model, so the engineer is asked. A machined STL is blocked until someone types the cycle time.
Why we test on real parts, not only test blocks
A steering knuckle once costed at £5.43 while every test passed. Six real production parts are now pinned, and a change that moves any of them fails the build.
Notes: On a job like this it is tempting to take the measuring and leave what looks like plumbing until later. These four checks are what make the rest safe. The price is always plain arithmetic, but a wrong input still gives a wrong price. The first check is the one to remember. The measured model is the ground truth. If anything fed to the cost contradicts the measured weight, it is flagged, and a big gap stops the costing. The second stops a thick, chunky part being costed as a pressing or a moulding. The third caps machining time on castings and forgings. The fourth is about honesty. Where the tool cannot know something, it asks rather than guessing. The red box is a lesson we learned the hard way. A steering knuckle once came out at five pounds forty-three while every test passed, because our tests used clean made-up shapes. Now six real production parts are pinned, and if a change moves any of them, the build fails.

## Slide 9
cv
CostVision
SHOULD-COST ENGINEERING
OPTION 1 · SETTINGS
Option 1: the fixed numbers inside the software
You asked what the hardcoded values actually are. These are engineering judgements written into the code. Six real ones, read off the software this month:
What it controls
Value
Why
Smallest face counted as machined
400 mm²
Below this we treat it as an edge, not a face to machine
Smallest pocket counted
80 mm²
Stops small recesses getting costed as pockets
Rework of a rejected plated part
USD 2.20 + 1.80 / m²
Strip-and-re-plate chemistry and effluent, on top of plating it again. The note on the stage reads 4-5x a first-pass part
Zinc price used for plating
USD 3.67 / kg
Market reference, August 2026. Moves monthly and is meant to get updated
Shape allowance, pressing
1.15
A real pressing has more surface than a flat plate: edges, flanges, bends
Shape allowance, casting and forging
1.25 / 1.10
Castings carry ribs and bosses; forgings are simpler on the outside
How they get handed over
Pulled out of the code into one list you can read and change without a developer. That list is a deliverable in its own right and it is a step in the Option 1 sequence.
Where these came from
They are our engineering estimates. They are not measurements from a JLR plant. Treat them as a starting point and expect to replace them as real data comes in.
Notes: Hardcoded values means nothing on its own, so here are six real ones, read off the software this month. The first two decide what counts as a machined face and what counts as a pocket. Look at the third row. Stripping and re-plating a rejected part is costed as its own stage: two dollars twenty of chemistry and one dollar eighty of effluent per square metre, on top of plating the part again. The note against it says the rework runs four to five times a first-pass part. That is why a three percent reject rate is nearer twelve to fifteen percent on cost. That is an engineering judgement, and exactly the sort of thing you would challenge in a review. So it should not be buried in code. We will pull every one of these into a single list you can read and change. The amber box is the caveat. These are our estimates, not measurements from one of our plants.

## Slide 10
cv
CostVision
SHOULD-COST ENGINEERING
OPTION 1 · DECISION FOR IT
Option 1: three ways to connect it to CAPEE
We do not know yet how CAPEE is built. Any of the three routes could work. The answer decides which one we use and how much effort it takes.
Route
Use when
What it means day to day
Relative effort
A · Put it inside CAPEE
CAPEE is built in JavaScript
Our code goes straight in. Only the measuring engine sits separately.
Least effort
B · Run it alongside
CAPEE is Java, .NET or anything else
It runs as its own service on a JLR server and CAPEE asks it for numbers over a secure link.
Most effort
C · Pass a file
CAPEE is a desktop or spreadsheet tool
It writes a file that CAPEE imports. Simplest to build, but somebody has to move the file.
Least effort
If we had to pick blind
Route B. It works whatever CAPEE turns out to be, and we can update CostVision without touching CAPEE every time.
Three questions for IT
What is CAPEE written in. Can it call another service on the network. Where can the measuring engine run: a server, or a laptop.
Effort is shown against the other two routes. None of the three has been sized by JLR.
Notes: I cannot give you one answer here, because nobody has told us how CAPEE is built. Rather than hold everything up, here are all three routes. Any of them could work. What changes is the effort, and I have shown that against each other rather than in weeks, because none of it has been sized. Route A puts our code inside CAPEE, which is easiest if CAPEE is built in JavaScript. Route B runs CostVision alongside as its own service, and CAPEE asks it for numbers. Route C just passes a file across, which is simple but needs someone to move the file. If you made me pick blind, I would take route B. It works whatever CAPEE is, and we can improve our side without touching CAPEE. The three questions in the amber box are what I need from IT to choose properly.

## Slide 11
cv
CostVision
SHOULD-COST ENGINEERING
OPTION 1 · THE TRIAL
Option 1: what the proof of concept proves
One part type, one team, 30 to 50 parts we have already bought. Four numbers come out of it, and none of them exist today.
1
How close is it?
Cost every part with the tool, compare against the price we actually paid, and report the average error. The test is whether the real price lands inside the range the tool itself gave for each part. A tool that is wrong and says so is usable. One that is wrong and confident is not.
2
How often does the engineer have to step in?
Count the values the engineer changed after the tool filled them, and the parts where the tool stopped and asked. Every part will ask for the material family, because a solid model cannot tell steel from aluminium. The rest we need to measure on JLR parts.
3
How much time does it save?
Time the same parts both ways: typed by hand into CAPEE, and filled by the tool with the engineer checking. The difference is the saving, measured rather than claimed.
4
What does it refuse, and was it right to?
Every part the tool turned down, with the reason. If it refuses parts it should have costed, that is a fault we need to see early.
Why it is worth doing even if the answer is disappointing
A measured accuracy figure is worth having either way. Today nobody can state one, so every conversation about this tool stalls in the same place.
Notes: This is what we would get out of the trial. I want to be concrete, because none of these four numbers exists today. First, how close is it. We cost the parts, compare with what we paid, and report the error. Every result in the tool comes with a range, a low and a high. The test I would use is whether the real price falls inside that range. A tool that is wrong and says so is usable. One that is wrong and confident is not. Second, how often the engineer steps in. Every part will ask for the material, because a solid model cannot tell steel from aluminium. In a bulk run that answer can come from the part list. The rest we need to count on JLR parts. Third, the time saving, measured by doing the same parts both ways. Fourth, what it refused and whether it was right to. The green strip is why it is worth doing even if the answer disappoints us.

## Slide 12
cv
CostVision
SHOULD-COST ENGINEERING
OPTION 1 · SEQUENCE
Option 1: order of work
1
Agree the connection
Find out how CAPEE is built, pick one of the three routes, agree exactly which numbers CAPEE expects.
2
Stand up the measuring software
Install it on a JLR server or laptop. Measure 20 real JLR parts and check the results against their drawings.
3
Hand over the settings list
Pull every fixed number into one list. JLR review it and sign it off before anything gets costed with it.
4
Move the safety checks across
The geometry checks and the questions the engineer confirms. In the scope from the start.
5
Connect into CAPEE
Wire it in, with AI left off. Cost one real part end to end.
6
Run the trial
One team, one part type, 30 to 50 parts with prices we paid. Produce the four numbers from the last slide.
Steps 1 and 2 can start together
Measuring does not depend on how CAPEE is built. Only step 5 does.
Start with one part type
Machined parts or pressings first. Widen it once it holds up.
Notes: Six steps, in the order they have to happen. Two are worth pulling out. Step three is the settings list. JLR reviews it and signs it off before anything is costed with it, so the judgements inside the tool are ours, not just mine. Step four is the safety checks. I have given them a step of their own so they do not get folded into the connection work and squeezed. Step five says AI stays off, which matches the build we have already given JLR. Nothing in Option one needs it. The blue box helps with planning. Steps one and two can run at the same time, because standing up the measuring software does not depend on knowing how CAPEE is built. Only step five does. The amber box is my suggestion for where to start: machined parts or pressings, because that is where most of our volume is and where we understand the shapes best.

## Slide 13
cv
CostVision
SHOULD-COST ENGINEERING
OPTION 2
Option 2: costing in bulk, unattended
WHAT WE DO TODAY
We cost the parts we have time to cost.
A basket of several hundred parts gets sampled, or
estimated by analogy against something similar, or
taken from what the supplier last quoted.
Nobody costs all of it from the geometry, because
there are not enough engineer-hours to do it.
WHAT OPTION 2 DOES
A list of parts goes in. Every one is measured,
costed and reported in one run, unattended.
An engineer is asked only where the geometry
cannot decide, and only once per question.
Same engine, same rate book, same geometry checks.
No AI anywhere in it.
What the run does, and what it does not
The part type comes from the list or from the measured shape. The material comes from the list. Where it cannot decide, it stops and asks rather than guessing. It never sets a price: every number comes from the same engine at the same rates. There is no AI in it, so it works in the JLR build.
Where this stands today
The run is built as a command-line tool. It writes the results, the open questions and a record naming the rate book it used. It has not yet been run on a JLR basket or on JLR rates, and there is no screen for it yet.
Notes: Option two is a different thing from Option one, and I want to be clear about that. Option one saves the engineer typing. Option two gives us something we do not have at all. Today we cost the parts we have time to cost. A basket of several hundred gets sampled or estimated by analogy, because there are not enough engineer-hours. Option two costs the whole basket in one run. The blue box says how. The part type comes from the list or from the shape. The material comes from the list. Where the tool cannot decide, it stops and asks, and one answer covers every part with the same question. There is no AI in it, so it runs in the JLR build as it is. The amber box is the honest position. The run is built, but only as a command-line tool, and it has never been run on our parts or our rates.

## Slide 14
cv
CostVision
SHOULD-COST ENGINEERING
OPTION 2
Option 2: what a bulk run does
What happens to a basket of parts, start to finish
A list goes in
Part numbers, CAD files, volumes, region
Each one measured
Same engine as a single part, in parallel
Rules fill the form
The part type’s own rules run
Only gaps escalate
One question, answered once, applied to all
Engine costs them
Eight buckets, every figure traceable
Three files out
Results, open questions and a run record
What a run produces, and how it stays honest
What
In short
Detail
Results file
One row per part
The eight cost buckets and the total
Questions file
Each open question once
Names every part it blocks, and the answer that clears them
Run record
The durable record
Inputs, answers, and the rule and rate-book versions used
Region
Rate book rebuilt for it
A region it does not know is refused, not guessed
Geometry checks
Same as a single part
A part that fails one is refused unless someone accepts it
Past rate books
All kept
Last quarter’s run can be redone on last quarter’s rates
The data is the work
Getting the part list, the CAD files and our own rates together is the real effort. We have not yet timed a JLR-sized basket.
Notes: Here is what a run does, start to finish. A list goes in, with part numbers, CAD files, volumes and the region each part is made in. Each part is measured by the same engine as a single part. The rules fill the form. Anything the tool cannot decide becomes a question, and each question appears once, naming every part it blocks. Then the engine costs them, in the same eight buckets as the screens. Three files come out: the results, the open questions, and a run record. The table is about trust. The run record names the rate book it used, and every rate book is kept. So a run from last quarter can be redone on last quarter's rates. A region it does not know is refused rather than quietly costed as the UK. The blue strip is the honest point. The hard part is gathering our data. I have not timed a basket of JLR size, so I will not quote a run time.

## Slide 15
cv
CostVision
SHOULD-COST ENGINEERING
OPTION 2 · PREREQUISITES
Option 2: what is built, and what is left
Most of the gaps on this list last time are now closed. This is where each one stands.
Item
Status
Detail
Type
A history of rate changes
Built
Every rate book is kept, not overwritten. A costing can name the book it used and be redone on it.
Done
A record of every bulk run
Built
Each run writes a record: inputs, answers, rule and rate-book versions. A costing done on screen is still kept only if someone saves it.
Done
Region and volume on the bulk route
Built
A region rebuilds the whole rate book for that country. Volume can be set per part or for the whole run.
Done
Gear and the geometry checks on the bulk route
Built
Gear is costed the same way on both routes. The same checks run, and a part that fails one is refused.
Done
JLR rates loaded
Not started
Until JLR's rate card is loaded through the Rate Converter, a run uses the built-in rate book of 16 June 2026.
Must have
A trial on a real basket, and maybe a screen
Not started
The run is a command-line tool today. A screen is optional. A trial on real JLR parts is not.
Next
The costing engine is the same one
The bulk run calls the same costing engine as the screens, with the same rate book and the same geometry checks.
Notes: Last time I showed you this slide it was a list of gaps. I would rather show you honestly where each one stands now. The first four are built. Every rate book is kept rather than overwritten, so a costing can name the book it used and be redone on it. Every bulk run writes a record of its inputs, answers and versions. One limit there: a costing done on the screen is still only kept if someone saves it. Region and volume now reach the bulk route, and so does gear, and the same geometry checks run on it. What is left is ours to do. The run has to be given JLR rates, loaded through the Rate Converter. Until then it uses the built-in book from June. And it needs a trial on a real basket. A screen is optional. The green strip is the reassurance. The bulk run is not a second costing engine. It calls the same one the screens use.

## Slide 16
cv
CostVision
SHOULD-COST ENGINEERING
OPTION 2 · THE CASE
Option 2: what it changes for the business
Today
With bulk costing
How many parts get a proper cost
The ones we have hours for
Every part in the list
How a basket gets priced
Sample and scale up
Every part costed from its own geometry
Turnaround on a new basket
Days of engineer time
Machine time, plus the data gathering
Consistency across a basket
Depends who costed it
Same rules and rates for every part
What we can say to a supplier
This is our estimate
Here is the build-up, per part, with the rates
Where an engineer spends the time
Typing numbers in
Answering the questions only a person can
What it needs from a person
One engineer per part
One answer per question, applied to every part
The honest limit on all of this
Every row assumes the tool is accurate enough to trust unattended, and today nobody can say whether it is. That is precisely what Option 1 measures, which is why it comes first.
No cost saving is claimed on this slide. The saving depends on our own rate data and on the accuracy figure Option 1 produces.
Notes: This is the business case for Option two. I have deliberately not put a pound figure on it. An honest one needs two things we do not have yet: our own rate data loaded, and the accuracy number from Option one. What I can show is what changes in kind. Today we cost the parts we have hours for and scale up from a sample. With bulk costing, every part in the list is costed from its own geometry, with the same rules and the same rates. What we can say to a supplier changes too. Instead of this is our estimate, it becomes here is the build-up, part by part. The row I would draw your eye to is the last one. Today it is one engineer per part. With this it is one answer per question, applied to every part it affects. The amber box is the limit on all of it. Every row assumes the tool is accurate enough to leave running, and that is exactly what Option one measures.

## Slide 17
cv
CostVision
SHOULD-COST ENGINEERING
OPTION 2 · SEQUENCE
Option 2: order of work
1
Load JLR rates
Materials, machine rates, labour, energy, country factors, through the JLR Rate Converter. Ours to do.
2
Agree who controls the rate book
Every rate book is already kept. JLR decides who may change rates and who signs them off.
3
Agree what a run record must hold
Each run already writes a record. JLR audit says whether it is enough, and where it is stored.
4
Check the bulk route on our parts
Region, volume, gear and the geometry checks are wired on. Confirm them on a handful of JLR parts.
5
Decide on a screen
The run is a command-line tool today. Add a screen only if the team needs one.
6
Trial on a real basket
One programme, one commodity family, run beside the way we cost today and compare.
Steps 2 and 3 are about control, not code
The tools exist. JLR decides who owns the rates and the records.
Step 1 can start now
Our own rate data helps both options, whatever is decided.
Notes: Six steps for Option two. Step one is loading our own rates, and it is worth starting whatever we decide, because both options need it. The Rate Converter takes JLR's rate card as it is exported and needs no macros. Steps two and three used to be software gaps. They are not any more. The tool keeps every rate book and writes a record of every run. What is left is a decision for JLR: who may change rates, who signs them off, and whether the run record is enough for audit. Step four is a check, not a build. Region, volume, gear and the geometry checks are wired on, and we should confirm them on a few of our own parts. Step five is a choice. The run works from the command line, so a screen is only worth building if the team wants one. Step six is a trial on a real basket, run beside how we cost today so we can compare.

## Slide 18
cv
CostVision
SHOULD-COST ENGINEERING
COMPARISON
The two options together
OPTION 1 · feed CAPEE
OPTION 2 · bulk costing
What it gives us
The engineer stops typing
We can cost a whole basket
Which system does the costing
CAPEE, same as now
CostVision engine, beside CAPEE
Does anyone learn a new tool
No, same CAPEE screens
A reviewer does, for the results
How much software work
Moderate: the CAPEE link
Less: the run is built
How much JLR data work
Parts with prices we paid
Our full rate book
Does it tell us how accurate we are
Yes, that is the point of it
It relies on that answer
Can we stop part way
Yes, CAPEE costs the same way either way
Yes, it runs alongside
Is it waiting on an unknown
Yes, how CAPEE is built
Yes, the accuracy figure
Is it audit-ready today
Yes, CAPEE keeps the record
Records exist; JLR has not reviewed them
Read the last two rows together
Option 1 gives the accuracy figure Option 2 leans on, and CAPEE keeps its record. Option 2 keeps records too, but JLR has not reviewed them. Hence this order.
No durations shown. Nothing in either option has been sized by JLR.
Notes: This puts the two side by side. The top half is fairly even, and each option wins some rows. One row has changed since last time. Option two used to be the bigger software job. Now the run is built, so most of its remaining work is data, not code. Option one still needs the link into CAPEE, and that waits on IT. The two rows I would look at are the last two. Option one produces the accuracy figure that Option two leans on. And Option one is audit-ready today, because CAPEE keeps the record exactly as it does now. Option two does keep its own records now, with the rate book each run used. But nobody at JLR has reviewed them against what audit needs. Those two rows are the whole argument for doing them in this order.

## Slide 19
cv
CostVision
SHOULD-COST ENGINEERING
RISKS
Risks and open items
Item
Applies to
Detail and what sorts it
Rating
We do not know how accurate it is
Both
Never compared against a price JLR has paid. The Option 1 trial is what settles it.
High
We do not know how CAPEE is built
Option 1
Holds up the choice of connection route. One answer from IT sorts it.
High
Run records not yet reviewed by JLR
Option 2
Rate books and run records are kept now. JLR audit has not said whether they are enough.
Medium
The built-in rates are not JLR rates
Both
The rate library is dated 16 June 2026. Until our card is loaded, costs use those rates.
Medium
The built-in numbers are our estimates
Both
Starting points, not JLR plant measurements. They get replaced as real data comes in.
Medium
The AI mode could be switched on
Both
The JLR build has no API key and neither option needs one. Adding a key turns AI on, so it needs an owner and approval first.
Low
Where the measuring engine runs
Option 1
Needs a standard Linux server or the Windows package. The cut-down Linux kind cannot run it.
Low
The tool is still changing
Both
It is under active development. For any trial we pin a version and stay on it.
Low
One decision deals with the top item
Approving the Option 1 trial turns "we do not know how accurate it is" into a number. Everything else on this list is smaller and has a known fix.
Notes: Eight items. The top one is the one that would stop me putting this in front of a supplier today, and approving the trial is what fixes it. The second is waiting on IT. The third is new. The software gap on records is closed, but JLR audit has not looked at them, so we should ask them early. The fourth matters more than it looks. Until our own rate card is loaded, every cost uses the built-in rates from June, and those are not our rates. The sixth is about AI, because it always comes up. There is no API key in the build we gave JLR, nothing is sent out, and neither option needs it. But turning it on is only a setting, so someone should own that switch. The last row is worth saying plainly. The tool is still being worked on, so for any trial we pin one version and stay on it.

## Slide 20
cv
CostVision
SHOULD-COST ENGINEERING
NEXT STEPS
What we need to get going
1
30 to 50 parts with the price we actually paid
Part, description, annual volume, where it was made, and the price paid. Existing purchase records will do. This is what turns "we think it is about right" into a number, and both options rest on it.
2
Our own rate data
Material prices, machine rates per hour, labour by grade, electricity and gas. The Rate Converter loads JLR's rate card as exported, with no macros. Worth starting now.
3
How CAPEE is built
What it is written in, whether it can call another service on the network, and what kind of server it runs on. Three questions to IT. Unblocks Option 1.
4
Agreement that AI stays off
Neither option needs AI, and the JLR build has no API key. If we want the AI features later, that is a separate approval.
5
A team and one part type for the trial
One cost engineer and one commodity family for the duration. Machined parts or pressings would be my choice.
The first two do not wait on any decision made today
Purchase records and our own rates are useful whichever way this goes.
Notes: Five things. The first is the one I will keep coming back to: thirty to fifty parts where we know what we paid. Purchase records are fine. I do not need anything new created. Without them I cannot tell anyone how accurate this is, and that is the first question we will be asked. The second is our own rates. The Rate Converter can take our rate card as it is exported today, with no macros, so this is mostly gathering, not building. It is worth starting whatever you decide, because both options need it. The third is three questions to IT. The fourth is a simple agreement. AI stays off. Neither option needs it, and the build JLR has already runs without it. If we ever want the AI features, that is a separate conversation and a separate approval. The fifth is a person and a part type for the trial. And the green strip: the first two do not wait on anything decided here.

## Slide 21
cv
CostVision
SHOULD-COST ENGINEERING
APPENDIX
Where the numbers come from
Every count in this pack was checked against the software on 28 September 2026.
Statement
How it was checked
19 manufacturing processes; 13 costed from CAD
Commodity modules and CAD rule packs in the code
About 12 to 70 values typed per part
Rough count of the input fields on CostVision's own forms, by commodity
Engine matches a hand calculation to under 0.01%
Reference machined bracket, £24.34, pinned in an automated test
6 real production parts pinned
A change that moves any of them fails the build
2,438 automated tests
Plus browser tests that cost every commodity and export Excel and PDF
Measuring makes no internet connection
Windows package runs offline and listens on this laptop only (127.0.0.1)
AI needs an API key in the JLR build
No key in the package; AI screens are hidden until one is added
A bulk run exists, with no AI
Command-line run: results, open questions and a run record
Every rate book is kept
Stored by a content fingerprint, so a past costing can be redone
Line counts on slide 7
Counted in the source files on 28 September 2026, rounded
Settings values on slide 9
Read off the software; each is a single defined value
328 materials, 178 machines, 42 labour grades
Rate library 2.1.0, dated 16 June 2026
20 manufacturing regions
Europe, UK, Turkey, the Americas and Asia, in the rate model
Sign-in and per-user data
Users see only their own saved work; a reset ends every old session
One number we deliberately do not show
Accuracy against real prices. The tool learns from logged actual prices, but none from JLR are loaded yet. That is ask number one.
Notes: Keep this one for anyone who wants to know how we know. Every claim in the pack was checked against the software this week rather than assumed. A few are worth pointing at. The engine's arithmetic matches a hand calculation to under 0.01 percent on a reference part. That proves the sums are right. It does not prove the price is right. Six real production parts are pinned, so we notice if a change moves them. The measuring makes no internet connection, and the Windows package only listens on the laptop itself. That is the answer to the first question IT security will ask. There is no API key in that build. The amber box is the one number I have deliberately left off every slide: accuracy against real prices. The tool can learn from actual prices once they are logged, but none from JLR are in it yet. That is why ask number one is what it is.